## Slide 1
Distribution System Restoration
Unknown Fault Discovery Simulator
Multi-Agent · Scout + RC + MPS · IEEE-13 Network
NYU
Tandon School of Engineering
SAI Lab · New York University
NYU Tandon · SAI Lab · Distribution System Restoration

## Slide 2
What We Built
IEEE-13 multi-agent DSR simulator with unknown fault discovery
NYU Tandon · SAI Lab · Distribution System Restoration
Network & Environment
▸ IEEE-13 bus network: 19 nodes, 8 loads, 2 switches
▸ TGraph (road routing) + EGraph (power flow)
▸ Faults: edge breaks or node damage, hidden from agents
▸ Outage zones: operator sees dark sections (SCADA), not exact faults
▸ Grid power recomputed each step via BFS
▸ 5 training cases with different fault combos
→
Agents & Coordination
▸ RepairCrew (RC): travels, discovers faults, repairs them
▸ Scout: fast search agent, sweeps unvisited outage nodes
▸ MPS: mobile power source, restores isolated islands
▸ Shared visited set — no two agents duplicate a node
▸ globally_claimed: prevents double-assignment mid-travel
▸ Known vs Unknown mode: compares optimal vs realistic

## Slide 3
What Went Wrong
Bugs found and fixed during development
NYU Tandon · SAI Lab · Distribution System Restoration
1
RCs idle at Step 0
Repair crews not dispatched at setup — wasted first hour. Fixed: kick RCs in setup().
2
Fault info leaked via EGraph
Agents guided by live/dead powered nodes → indirectly knew fault locations. Fixed: use explicit outage_zones.
3
Switch nodes as faults
S1 / S2 marked as fault sites but they are switches, not buses. Fixed: redesigned all 5 cases.
4
Duplicate node visits
Two agents sent to same node because global_visited only updated on arrival. Fixed: add globally_claimed set.
5
RC assignment race condition
RC2 standing on fault not counted — RC1 also sent there. Fixed: _rc_at_fault() check in assignment loop.
6
Large unknown overhead (open)
Cases 3 & 5 hit 50-step limit in unknown mode (+39h / +43h). Root cause: RC assignment logic still misses some faults.
⬡ Issue 6 is still open

## Slide 4
Future Work
From heuristic simulator to LLM-guided restoration
NYU Tandon · SAI Lab · Distribution System Restoration
1
1 Fix & Scale Simulator
▸ Fix remaining RC assignment bug (unknown overhead Cases 3 & 5)
▸ Add IEEE-33 network (45 nodes, 31 loads)
▸ Run 1000+ episodes per case
▸ Export (state, action, reward) as JSONL for supervised training
▸ Benchmark: greedy vs random vs optimal
2
2 Fine-Tune LLM
▸ SFT on known-fault optimal trajectories
▸ LoRA adapter on top of base LLM (Qwen 7B / LLaMA 3)
▸ Input: grid state as structured text prompt (nodes, faults, agent positions)
▸ Output: next best action for each RC / MPS
▸ Reward signal: weighted loads restored / time
3
3 Evaluate & Deploy
▸ Test LLM on unseen unknown-fault cases
▸ Goal: close the discovery overhead gap (~5–8h extra vs known baseline)
▸ Compare: LLM vs greedy vs random
▸ Extend to multi-fault, multi-crew scenarios
▸ Real-time operator decision support tool